## Slide 1: LSODA Stiff Solver
Arjun Ray Undergraduate Research Assistant I
rayarjun@frib.msu.edu
14 August 2025

## Slide 2: LSODA.cpp
LSODA stands for Livermore Solver for Ordinary Differential equations with Automatic method switching written by Alan C. Hindmarsh and Linda R. Petzold.
Paper – https://computing.llnl.gov/sites/default/files/ODEPACK_pub1_u88007.pdf
LSODA Features
Hybrid Solver – Combines two methods: fast Adams predictor–corrector for nonstiff regions and stable implicit Backwards Differentiation (BDF) for stiff regions, switching automatically when stiffness is detected.
Stiffness Detection – Monitors error growth vs. step size; switches to BDF before instability occurs, so it never wastes time taking thousands of tiny steps like ode.cpp.
Adaptive Step Size & Order – Continuously tunes both step length and polynomial order for efficiency and accuracy, ensuring minimal computation while meeting tolerance requirements.
Banded Jacobian Support – Can exploit narrow bandwidth in ETACHA’s Jacobian, cutting stiff-solve cost and giving massive speed-ups for large systems.

## Slide 3: Implementation
Why LSODA Needs Banded Jacobians
Banded LU slashes cost and memory(~60%).
Potentially 1000× faster in stiff phases.
Why LSODA is Faster When Stiff
Detects stiffness early, switches to large stable implicit steps.
ode.cpp shrinks steps until max-step error; LSODA leaps over stiff bottleneck.
LSODA Advantages
Euler, Adams PECE, RK45 all work well for non-stiff problems but fail or become extremely slow when stiffness appears.
LSODA automatically switches between non-stiff (Adams) and stiff (BDF) methods, so it can handle both without user intervention.
LSODA.cpp is around 60% faster than the original Fortran version EQDIF.for.